## Slide 1
Sampler-Crow
Portable Music Workstation — Build Guide v3
Teensy 4.1 + Audio Shield + CrowPanel 5" + Novation Launchpad
8-TRACK
SEQUENCER
USB MIDI
HOST
TRS LINE
IN/OUT
SAMPLE
PLAYBACK
Updated: 2026-04-11 • github.com/nohumans-com/Sampler-Crow

## Slide 2
What you will build
A standalone drum machine + sampler + synth that runs without a computer
8 independent tracks (kick / snare / hats / clap / bass / lead / pluck / fx)
Step sequencer with 8 steps per track, BPM clock, pattern save/load
Real Novation Launchpad Mini MK3 as the step editor and clip launcher
CrowPanel 5" touchscreen as the visual UI (mixer, piano roll, samples)
Analog stereo TRS line in, line out, and headphone out
5-pin TRS MIDI in and MIDI out
Companion macOS host app for development, monitoring, sample loading

## Slide 3
System architecture
Two processors + Audio Shield + powered USB hub
CrowPanel 5.0" HMI
ESP32-S3-WROOM-1 | 800×480 touch | LVGL UI
Teensy 4.1 + Audio Shield
ARM Cortex-M7 @ 600 MHz • SGTL5000 codec
Audio engine • Sequencer • Sample playback
USB Host (MIDI) • USB Device (Audio+MIDI+Serial)
MIDI TRS UART • SD card • 4 pots, 4 buttons
LAUNCHPAD
Mini MK3
USB HUB
(powered)
MIDI TRS
in/out
LINE TRS
in/out/hp
µSD
samples
macOS
host app

## Slide 4
Bill of Materials (1/2)
Core components + audio/MIDI I/O • all-in total ~$245
Part
Product
Price
Link
Teensy 4.1 (with pins)
PJRC Teensy 4.1 ARM Cortex-M7 600 MHz
$49
View product →
Audio Shield Rev D
Teensy Audio Shield (SGTL5000)
$14
View product →
CrowPanel 5.0" HMI
Elecrow ESP32-S3 800x480 cap touch
$60
View product →
Novation Launchpad Mini 3
Novation LAUNCHPADMINIMK3
$109
View product →
ubld.it MIDI Breakout MV
Opto-isolated MIDI I/O, 3.3/5 V
$25
View product →
3.5 mm TRS jacks (5-pack)
Panel mount stereo jacks
$7
View product →
MicroSD 32 GB
SanDisk Ultra 32 GB
$8
View product →

## Slide 5
Bill of Materials (2/2)
USB host + power + controls • pick ONE power option
Part
Product
Price
Link
SparkFun USB Host Cable
5-pin to USB-A female (Teensy 4.1)
$4
View product →
Powered USB hub
Anker 4-Port USB 2.0 Hub with AC adapter
$15
View product →
USB-C panel mount (2x)
USB-C male-to-female pigtails
$8
View product →
B10K potentiometers
×4 with knobs (20-pack)
$9
View product →
Tactile buttons
12 mm momentary ×4 (25-pack)
$7
View product →
Perfboard + hookup wire
Proto PCB + 22 AWG solid core
$18
View product →
POWER — pick ONE of these four options
A: Wall wart 5V/3A
Mean Well GSM18A05-P1J + barrel jack + perfboard
$19
View product →
B: Internal AC-DC
Mean Well IRM-20-5 (20W, 5V/4A, enclosed) + C8 inlet
$21
View product →
C: USB-C PD input
Adafruit HUSB238 breakout (any PD charger)
$14
View product →
D: Buck regulator
Pololu D36V28F5 (5V/3.2A) + 9-12V brick
$25
View product →

## Slide 6
Power strategy
Current budget • distribution • critical wiring rules
Current budget @ 5 V
Load
Typical
Peak
Teensy 4.1 + Audio Shield
120 mA
180 mA
CrowPanel 5" (backlight)
250 mA
400 mA
Launchpad Mini MK3
200 mA
500 mA
Powered USB hub + expansion
30 mA
550 mA
Pots, buttons, misc
10 mA
10 mA
TOTAL
~610 mA
~1.64 A
Recommend 5 V / 3 A supply (comfortable headroom)
Critical wiring rules
1.
Cut the VUSB→VIN pad underneath the Teensy 4.1 before
powering from VIN. Standard PJRC procedure, one scalpel cut.
2.
DO NOT back-feed the USB-C COMPUTER port from your
5 V rail. It is a device port. Leave VBUS for enumeration only.
3.
The USB hub must be POWERED from the system 5 V rail
via its own polyfuse, NOT from the Teensy USB host 5V pad.
4.
Add a 1N5819 Schottky diode on the barrel jack input for
reverse-polarity protection. Cheap insurance.
5.
Add a 1000 µF bulk cap near the distribution block to
absorb the Launchpad LED inrush spike.

## Slide 7
Panel layout
Front = display + controls • Rear = all I/O
FRONT PANEL
5" Touchscreen 800×480
P1
P2
P3
P4
B1
B2
B3
B4
REAR PANEL
5V DC
IN
USB-C
COMPUTER
USB-C
CTRLR
LINE
IN
LINE
OUT
HEAD
PHONE
MIDI
OUT
MIDI
IN
Note: USB-C COMPUTER is a DEVICE port (host your laptop sees). USB-C CTRLR is for the Launchpad via the internal powered hub.

## Slide 8
Step 1: Audio Shield + controls
Stack the Audio Shield, wire 4 pots and 4 buttons, verify tone output
1. Stack the Audio Shield onto the Teensy 4.1 (no soldering — just press).
2. Wire each pot: outer legs to GND and 3.3 V, wiper to analog input.
3. Wire each button: pin to GND (uses INPUT_PULLUP in software).
4. Upload firmware from firmware/ directory, hear 440 Hz test tone.
Pin map
Pin A2 (16)
Pot 1 wiper
Cutoff
Pin A3 (17)
Pot 2 wiper
Resonance
Pin A4 (24)
Pot 3 wiper
Attack / Decay
Pin A5 (25)
Pot 4 wiper
Volume / Mix
Pin D2
Button 1 → GND
Play / Trigger
Pin D6
Button 2 → GND
Record
Pin D9
Button 3 → GND
Mode / Preset
Pin D22
Button 4 → GND
Shift / Function

## Slide 9
Step 2: USB host + MIDI
Solder the 5-pin USB host header, wire the MIDI breakout board
USB host pads (bottom of Teensy 4.1)
• Solder 5-pin male header to the bottom pads labeled "USB HOST"
• Connect SparkFun USB Host Cable or direct-wire to powered USB hub
• IMPORTANT: use only the D+, D-, GND pads — leave the 5V pad disconnected
• Wire hub VBUS IN directly from system 5 V rail through a 1 A polyfuse
ubld.it MIDI breakout (TRS Type A)
• Set the board voltage switch to 3.3 V
• ubld.it TX ← Teensy Pin 14 (Serial3 TX) — MIDI OUT data
• ubld.it RX → Teensy Pin 15 (Serial3 RX) — MIDI IN data
• ubld.it VCC → Teensy 3.3 V
• ubld.it GND → Teensy GND
• Panel-mount the two 3.5 mm TRS jacks to the board's MIDI IN / OUT
⚠ TRS Type A standard: Tip = current source, Ring = current sink, Sleeve = GND

## Slide 10
Step 3: Power distribution
Wire up the barrel jack → distribution board → everything
Build the tiny distribution board on a piece of perfboard
1.
Cut the VUSB→VIN pad on the underside of the Teensy 4.1 with a sharp hobby knife.
2.
Panel-mount the 2.1 × 5.5 mm barrel jack on the rear panel.
3.
On perfboard: barrel jack (+) → 1N5819 Schottky diode → node X.
4.
From node X: 1000 µF / 16 V electrolytic cap (+ to X, – to GND).
5.
From node X: 1.5 A polyfuse → 5 V MAIN rail screw terminal.
6.
From node X: 1 A polyfuse → 5 V HUB rail screw terminal.
7.
Wire 5 V MAIN to Teensy VIN (5 V pin) and CrowPanel 5 V in.
8.
Wire 5 V HUB to the powered USB hub's VBUS input.
9.
Wire barrel jack (−) and everything else GND to a common ground bus.
10.
Verify with multimeter: 5 V ± 0.1 V at Teensy VIN under load.
⚠ Leave the USB-C COMPUTER port's VBUS disconnected. Do NOT back-feed.

## Slide 11
Which power option should you choose?
Four real products, pick based on your budget and aesthetic
A
Wall wart + barrel jack
Cheapest • simplest • works
Mean Well GSM18A05-P1J
5 V / 3 A external brick
+ barrel jack + small perfboard
$19
Recommended for prototype
B
Internal AC-DC module
Professional • self-contained
Mean Well IRM-20-5
5 V / 4 A encapsulated
+ C8 mains inlet
$21
Recommended for final build
C
USB-C PD input
Modern • phone charger works
Adafruit HUSB238 breakout
negotiates 5 V / 3 A from
any USB-C PD charger
$14
If you want a single USB cable
D
Buck regulator
Maximum headroom
Pololu D36V28F5
5 V / 3.2 A switcher
+ 9-12 V wall brick
$25
If you plan to add a power amp

## Slide 12
Step 4: Firmware & host app
Flash the Teensy, build the macOS app, start making beats
Firmware (Teensy 4.1)
Requires PlatformIO with Python 3.13 (not 3.14)
$ cd ~/Sampler-Crow
$ pio run
# Put Teensy in bootloader mode
# (press the button on the board)
$ teensy_loader_cli --mcu=TEENSY41 \
-w -v .pio/build/teensy41/firmware.hex
# Or just:
$ pio run -t upload
macOS host app
SwiftUI • Swift 6 • macOS 15+
$ cd SamplerCrowApp
$ swift build -c release
# Deploy to /Applications
$ cp .build/release/SamplerCrowApp \
"/Applications/Sampler Crow.app/\
Contents/MacOS/Sampler Crow"
$ xattr -cr "/Applications/Sampler Crow.app"
$ codesign --force --sign - \
"/Applications/Sampler Crow.app/\
Contents/MacOS/Sampler Crow"
$ open "/Applications/Sampler Crow.app"
Plug in a Novation Launchpad Mini MK3 → pick your audio interface in the Audio tab → press Play.

## Slide 13
Why we are NOT hosting a USB audio interface
The honest technical answer — read this before asking again
What you might think you want
"Plug a Universal Audio Volt 476 into the Sampler-Crow's USB host port, get 8 channels of high-end preamp inputs routed straight into the sampler engine."
Why it does not work on the Teensy 4.1
USBHost_t36 library has ZERO USB Audio Class host driver. Checked the source.
AudioInputUSB / AudioOutputUSB in the Teensy Audio Library are DEVICE mode only.
USB Audio Class 2 uses isochronous transfers at 480 Mbps with clock feedback — far beyond USB MIDI bulk transfers.
Even if the driver existed, handling 8×44.1kHz streams while running the sampler engine is borderline CPU-wise.
The ESP32-S3 bridge in v2 was even worse: full-speed 12 Mbps USB only, 2-channel max experimental support.
What the pros do instead
Dirtywave M8, Teenage Engineering OP-1, Polyend Tracker, Elektron Syntakt, Elektron Digitakt II — ALL of these professional portable instruments use an on-board codec, not USB audio hosting. When they need to integrate with a computer-based studio, they present themselves AS a USB audio device. That is the pattern Sampler-Crow follows: the Audio Shield SGTL5000 handles TRS I/O, and the Teensy's USB device port exposes us as an audio device to any Mac or PC alongside your Volt.

## Slide 14
Roadmap
Where we are and where we are going
✓
Phase 1-6
Foundation, sequencer, Launchpad integration
✓
Phase 7a
8-voice multi-timbral synth (kick/snare/hats/bass/lead)
✓
Phase 7b
Functional mixer: volume, mute, solo per track
→
Phase 7c
Velocity / pitch per step editing
→
Phase 8
Drum sampler: WAV playback from SD card (DrumMode port)
Phase 9
Pattern save/load to SD as JSON
Phase 10
Mutable Instruments Plaits synth integration
Phase 11
Chord progression sequencer + scale quantizer
Phase 12
Port 5 sampler modes from new_hits (Pitch/Grain/Chop/Drum/Multi)
Phase 13
CrowPanel 5" LVGL touchscreen UI
Phase 14
Effects per track + AUX sends + master bus
Phase 15
Live looping on audio tracks

## Slide 15
Links & references
Everything you need is on the repo
Project repository
https://github.com/nohumans-com/Sampler-Crow
Key documents in the repo
HARDWARE_DESIGN.md
Full v3 hardware spec — definitive source
SOFTWARE_DESIGN.md
Original software architecture
STATUS.md
Current build state and roadmap
firmware/
Teensy 4.1 firmware (PlatformIO + Arduino)
SamplerCrowApp/
macOS host app (SwiftUI + Swift 6)
Teensy 4.1 reference
PJRC Teensy 4.1
https://www.pjrc.com/store/teensy41.html
Audio Library
https://www.pjrc.com/teensy/td_libs_Audio.html
USBHost_t36
https://github.com/PaulStoffregen/USBHost_t36
USB host cable
https://www.sparkfun.com/usb-host-cable-for-teensy-4-1-and-teensy-3-6.html